## Slide 1: Quantitative Methods Surface Area
Module No. Cons 1012
Lecturer Jennifer Byrne

## Slide 2
Last week we got a question to calculate the cost of painting the surface area of room.
Walls (4) 2 x 4.5 x 2.7 = 24.3
2 x 3.6 x 2.7 = 19.44
43.74m²
Instead we can add the length and breath together and then x 2 x H.
2(L + B) x H = Surface Area
2(4.5+3.6) x 2.7 = 43.74m²
When calculating surface area you can assume the top and bottom of the shapes are left open unless the question states to include them.
Surface Area
4.5m
2.7m
3.6m

## Slide 3
Q 1. Calculate the surface area of the cuboid.
Q 2. Calculate the surface area of the cube.
Q 3. Calculate the surface area of the cylinder.
Surface Area
3.75m
2.4m
2.6m
3.50m
Diameter 5m
1.4m

## Slide 4
Q 1. Calculate the surface area of the cuboid.
2(L + B) x H = Surface Area
2 (3.75 + 2.6) x 2.4 = 30.48m²
Q 2. Calculate the surface area of the cube
2(L + B) x H = Surface Area
2(3.5 + 3.5) x 3.5 = 49m²
Q 3. Calculate the surface area of the cylinder.
2rH = Surface Area
2 x  x 2.5 X 1.4 = 21.991m²
Surface Area
3.75m
2.4m
2.6m
3.50m
Diameter 5m
1.4m

## Slide 5: Surface Area of Sphere
Calculate the surface area of the Sphere.
Formula: Surface Area = 4  r²
4 x  x 2² = 4 x  x 2² = 50.26m²
Q 1. Calculate the surface area of the Sphere A. A
Q 2. Calculate the surface area of the Sphere B. B
Radius = 2m
Radius = 3.75m
Diameter = 7.5m

## Slide 6: Surface Area of Sphere
Calculate the surface area of the Sphere.
Formula: Surface Area = 4  r²
4 x  x 2² = 4 x  x 2² = 50.26m²
Q 1. Calculate the surface area of the Sphere A. A
4 x  x 3.75² = 4 x  x 3.75² = 176.714m²
Q 2. Calculate the surface area of the Sphere B. B
4 x  x 3.75² = 4 x  x 3.75² = 176.714m²
Radius = 2m
Radius = 3.75m
Diameter = 7.5m

## Slide 7: Surface Area of Cones
NOTE: When working with cones you need vertical height to calculate volume and sloping side length to calculate surface area. If you only have one of these you may need to work out the other.
E.g. 1. Calculate the surface area of the Cone.
Formula: Surface Area =  r l (l = sloping length)
 x 2 x 3.6 = 22.619m²
E.g.2. Calculate the surface area of the Cone.
First, we need sloping height Pythagoras Theorem a² + b² = c²
2² + 3.6² = 16.96²
√16.96 = l = 4.118m
 x 2 x 4.118 = 25.874m²
2m
3.6m
2m
3.6m

## Slide 8: Surface Area of Cones
Q 1. Calculate the surface area of the Cone.
Formula: Surface Area =  r l (l = sloping length)
Q 2. Calculate the surface area of the Cone.
First, we need sloping height Pythagoras Theorem a² + b² = c²
3.2m
4.5m
2.2m
2.6m

## Slide 9: Surface Area of Cones
Q 1. Calculate the surface area of the Cone.
Formula: Surface Area =  r l (l = sloping length)
 x 3.2 x 4.5 = 45.238m²
Q 2. Calculate the surface area of the Cone.
First, we need sloping height Pythagoras Theorem a² + b² = c²
2.2² + 2.6² = x²
4.84 +6.76 = 11.6
√11.6 = l = 3.405m
 x 2.2 x 3.405= 23.533m²
3.2m
4.5m
2.2m
2.6m

## Slide 10: Surface Area of Truncated Cones
NOTE: (for frustum we need to get full cone and take off the piece we don't have)
Truncated cones are half full height.
Formula: Surface Area =  R L-  r l
Q6. Calculate the surface area of the truncated cone.
( R L)- ( r l) =
( x 0.6 x 1.0) – ( x 0.3 x 0.5) =
1.885 – 0.471 = 1.414m²
Or
Frustum of truncated cone
Formula (r + R)l
 (0.3 + 0.6) x 0.5 = 1.414m²
0.3m
0.5m
0.6m
1.0m

## Slide 11: Surface Area of Truncated Cones
Q6. Calculate the surface area of the Truncated Cone.
Formula: Surface Area =  R L-  r l
( x 0.4 x 3.0) – ( x 0.2 x 1.5) =
3.769 – 0.942 = 2.827m²
Or
Frustum of truncated cone
Formula (r + R)l
 (0.2 + 0.4) x 1.5 = 2.827m²
0.2m
1.5m
0.4m

## Slide 12: Surface Area of Truncated Cones
NOTE: if we are not given the Slope length then we must find it using Pythagoras Theorem a² + b² = c²
2² + 6² = 40
√40= l = 6.325m
Formula (r + R)l
 (2 + 4) x 6.325 = 119.223m²
Q1. Calculate the surface area of the truncated Cone
3² + 4² = 25
√25= l = 5m
Formula (r + R)l
 (2 + 5) x 5= 109.95m²
2m
6m
4m
6m
2m
5m
2m
4m
3m
4m