## Slide 1: Quantitative Methods Transformation of Formulae
Module No. Cons 1012
Lecturer Jennifer Byrne

## Slide 2: Transformation of Formulae
A formula is a mathematical expression in which symbols are used to solve problems for example Area of a circle = πR².
Write down the formula and put in any information that is known.
The formula can then be calculated out to give the answer.
Sometimes a formula has to be rearranged before a calculation can be carried out. This rearranging process is called transposing the formula.
When transposing a formula any part of it can be moved from one side of the equals sign to the other, but in doing so, each part of the formula that crosses the equals sign becomes the opposite of itself ie. plus sign changes to a minus, multiplication to division etc.
Before transposing the formula the subject of the formula (unknown value) should be placed on the left hand side.

## Slide 3: Transformation of Formulae
Example 1 Express “ c ” as the subject
a = b + c + d
b + c + d = a
c = a – b – d
Example 2 Express “ b ” as the subject
x + y = a – b + c
a – b + c = x + y
– b = x + y – a – c
You can’t have a negative number as your subject so both sides will have to be multiplied by = ( – 1 )
b = – x – y + a + c
It is usual to express the positive numbers before the negative ones.
Answer
b = a + c –x – y

## Slide 4: Transformation of Formulae Square
Example 1: Calculate the perimeter of the square.
The area of a square is 121m²
We need to get the square root of this number so find this symbol
√121 = 11m one side is 11m
Perm. 11 x 4 = 44m Ans Perm. is 44m
Example 2: Calculate the perimeter of the square.
The area of a square is 66m²
√66 = 8.12m one side is 8.12m
Perm. 8.12 x 4 =32.48m Ans Perm. is 32.48m
Example 3: Calculate the perimeter of the rectangle.
The area of a rectangle is 48m² short side is 6m
48 ÷ 6 = 8m
Perm. (6 + 8) x 2 = 28m Ans Perm. is 28m

## Slide 5: Transformation of Formulae Triangle
Example 1: Given the area and base Calculate the Perpendicular height.
Area 72m² Base 12m
Area of Triangle : ½ Base x Perp. Height
½ base x Perp. Height = Area
Perp. Height = Area ÷ ½ Base
Perp. Height = 72 ÷6
Perp. Height = 12m Ans Perp. Height is 12m
Example 2: Given the area and Perp. height calculate the base.
Area 159.5m² Perp. Height 22m
Area of Triangle : ½ base x Perp. Height
½ Base x Perp. Height = Area
½ Base = Area ÷ Perp. Height
½ Base = 159.5 ÷ 22
½ Base = 7.25m
Base = 7.25 x 2 = 14.5m Ans Base is 14.5m

## Slide 6: Transformation of Formulae Circle
Example 1: Given Circumference 37.68m find the radius.
37.68m = 2 x 3.14 X r
37.68 ÷2 = 3.14 x r
  18.84=3.14 x r
18.84 ÷ 3.14 = 6m
Ans radius is 6m
Example 2: Given Circumference 125.68m find the radius.
125.68m = 2 x 3.14 X r
125.68m ÷ 2 = 3.14 X r
62.84 = 3.14 x r
62.84 ÷ 3.14 = 20.01m
Ans radius is 20m

## Slide 7: Transformation of Formulae Circle
Example 3: If the area of a circle is 0.866m²
What is the radius of the circle?
πr² = 0.866 ÷ π = 0.275
√ 0.275 = 0.525 = r
Calculate the length of the circumference
2πr = 2 x π x 0.525 = 3.298m
Example 4: If the circumference of a circle is 2.3m in length.
Determine the length of the radius.
2πr = 2.3 ÷ 2 = 1.15 ÷ π = 0.366m = r
Determine the area of the circle
πr² = π x 0.366² = 0.42m²