## Slide 1: Quantitative Methods Volume
Module No. Cons 1012
Lecturer Jennifer Byrne

## Slide 2
The Volume of an object is the amount of space that it occupies.
The S.I. Unit for volume is the cubic metre
The S.I. Symbol for volume is m³
Rectangular Solids
Length x Width x Height
5.5 x 4 x 6.5 = 143m³
The Cylinder
Area of Base x Height
π x 4² x 6 = 301.59 m³
Volume

## Slide 3
The S.I. Symbol for volume is m³
Length x Breadth x Height
L x B x H = Volume
4.5 x 3.6 x 2.7 = 43.74m³
When calculating Volume you should bring all measurements to the same SI unit.
23cm = 0.23m
23mm = 0.023m
Volume
4.5m
2.7m
3.6m

## Slide 4
Q 1. Calculate the Volume of the cuboid.
Q 2. Calculate the Volume of the cube.
Q 3. Calculate the Volume of the cylinder.
Volume
3.75m
2.4m
2.6m
3.50m
Diameter 5m
1.4m

## Slide 5
Q 1. Calculate Volume of the cuboid.
L x B x H = Volume
3.75 x 2.6 x 2.4 = 23.4m³
Q 2. Calculate the Volume of the cube
L x B x H = Volume
3.5 x 3.5 x 3.5 = 42.875m³
Q 3. Calculate the Volume of the cylinder.
 r²h = Volume
 x 2.5² X 1.4 = 27.48m³
Volume
3.75m
2.4m
2.6m
3.50m
Diameter 5m
1.4m

## Slide 6: Volume of Sphere
Calculate the Volume of the Sphere.
Formula: Volume = 4  r³ 3
4 x  x 2³ = 100.53 = 33.510m³ 3 3
Q 1. Calculate the Volume of the Sphere A. A
Q 2. Calculate the Volume of the Sphere B. B
Radius = 2m
Radius = 3.75m
Diameter = 7.5m

## Slide 7: Volume of Sphere
Calculate the Volume of the Sphere.
4 x  x 2³ = 100.53 = 33.510m³ 3 3
Q 1. Calculate the Volume of the Sphere A. A
4 x  x 3.75³ = 662.679 = 220.893m³ 3 3
Q 2. Calculate the Volume of the Sphere B. B
4 x  x 3.75³ = 662.679 = 220.893m³ 3 3
Radius = 2m
Radius = 3.75m
Diameter = 7.5m

## Slide 8: Volume of Cones
NOTE: When working with cones you need vertical height to calculate volume and sloping side length to calculate surface area. If you only have one of these, you may need to work out the other.
E.g. 1. Calculate the volume of the Cone.
Formula: = ⅓  r² h
⅓ x  x 2² x 3.6 = 15.079m³
E.g.2. Calculate the Volume of the Cone.
First, we need the height Pythagoras Theorem a² + b² = c²
3.6² - 2² = 8.96
√8.96 = 2.99m
⅓ x  x 2² x 2.99 = 12.511m³
2m
3.6m
2m
3.6m

## Slide 9: Volume of Cones
Q 1. Calculate the Volume of the Cone.
Formula: Volume = ⅓  r² h
First, we need height Pythagoras Theorem a² + b² = c²
Q 2. Calculate the Volume of the Cone.
3.2m
4.5m
2.2m
2.6m

## Slide 10: Volume of Cones
Q 1. Calculate the Volume of the Cone.
Formula: Volume = ⅓  r² h
First, we need height Pythagoras Theorem a² + b² = c²
4.5² - 3.2² = 10.01
√10.01 = 3.16m
⅓ x  x 3.2² x 3.16 = 33.85m³
Q 2. Calculate the Volume of the Cone.
⅓ x  x 2.2² x 2.6 = 13.16m³
3.2m
4.5m
2.2m
2.6m

## Slide 11: Volume of Truncated Cones
Q7. Calculate the Volume of the Truncated Cone.
Formula: Volume = ⅓  h(R²+{Rr}+r²)
Volume = ⅓  6 (4² + {4 x 2} + 2²)
= ⅓ x  x 6 (28)
= 175.929m³
2m
6m
4m

## Slide 12: Volume of Truncated Cones
NOTE: if we are not given the height then we must find it using Pythagoras Theorem a² + b² = c²
Q 6. 0.5² - 0.3² = 0.16 √0.16 =0.4m
Volume = ⅓  h(R²+{Rr}+r²)
Volume = ⅓  0.4 (0.6² + {0.6 x 0.3} + 0.3²)
⅓ x  x 0.4 x (0.63) = 0.264m³
Calculate the Volume of the Truncated Cone
Formula: Volume = ⅓  h(R²+{Rr}+r²)
Volume = ⅓  4 (5² + {5 x 2} + 2²)
= ⅓ x  x 4 (39)
= 163.36m³
0.3m
0.5m
0.6m
0.5m
0.3m
5m
2m
4m