## Slide 1: Quantitative Methods Volume, Mass & Density
Module No. Cons 1012
Lecturer Jennifer Byrne

## Slide 2: Volume, Mass and Density
Mass refers to the weight of an object and is measured in Kilogram’s(kg)
Density is mass per unit volume and is measured in Kg/m³
If the volume and density of a material is known, the mass(weight) can be calculated:
Mass = Density x Volume
(This formula can also be expressed for Mass or Volume through transposition)

## Slide 3: Volume, Mass and Density
To get the Weight or Mass of something you multiply the volume by its Density
Example:
Calculate the weight of the plank size 2.4m x 200mm x 75mm if the density is 470 kg/m³
Volume: 2.4 x 0.2 x 0.075 = 0.036m³
Weight: 0.036 x 470 = 16.92Kg

## Slide 4: Volume, Mass and Density
To get the Density of something you divide the Weight by the Volume
Example:
A clay brick measuring 215mm x 100mm x 65mm weighs 2.7Kg
Calculate the density of the brick.
Volume: 0.215 x 0.10 x 0.065 = 0.00139m³
Density: 2.7 ÷ 0.00139 = 1942.446kg/m³

## Slide 5: Volume, Mass and Density
Q 1 A concrete block measures 440mm x 215mmx 100mm .
Calculate the weight of the block if the density of the concrete is 2300kg/m³
(0.44 x 0.215 x 0.10 ) x 2300 = 21.76kg
Q 2 Calculate the weight of a wall 4.5m long x 2.5m high where blocks are laid flat. Density of the concrete is 2300kg/m³
(4.5 x 2.5 x 0.215 ) x 2300 = 5563.12kg

## Slide 6: Volume, Mass and Density
Mass = Density x Volume
Example: Calculate the volume of concrete required for the cylindrical column shown, and from this, calculate the weight of the column if the density concrete is 2400 kg/m³
(Vol. of cylinder =  r² h)
Answer: Volume =  r² h
=  x 0.25² x 4 = 0.785m³
Mass = Density x Volume
= 2400 x 0.785 = 1884kg
Diameter 500mm
Height
4m

## Slide 7
Q.3 Calculate the mass (weight) of the timbers listed below:
Norway Spruce (white deal) Density = 470 kg/m³
European Redwood (red deal) Density = 515 kg/m³
American Red Oak Density = 790 kg/m³
Greenheart Density = 1040kg/m³
Mass = Density x Volume
Volume, Mass and Density
2.16m
5cm
250mm

## Slide 8
First find volume of plank L x B x W
Volume of plank = 2.16m x 0.250mm x 0.050mm = 0.027m³
(Mass = Density x Volume)
Norway Spruce = 0.027 x 470 = 12.69 kg
European Redwood = 0.027 x 515 = 13.905kg
American Red Oak = 0.027 x 790 = 21.33kg
Greenheart = 0.027 x 1040 = 28.08 kg
Volume, Mass and Density