## Slide 1: Quantitative Methods Costings
Module No. Cons 1012
Lecturer Jennifer Byrne

## Slide 2: Costings 4 Worksheet
To find the total costings always read the question carefully and calculate the answer in order of the question.
Q. 1 Calculate the cost of slating the lean-to roof shown if the cost of slating is €30.68 per m²
Allow 15% for waste.
Answer:
7.5 x 4.8 x €30.68 = € 1104.48
1104.48 + 15% = €1270.15
Or
7.5 X 4.8 = 36 + 15% = 41.4
41.4 X 30.68 = €1270.15

## Slide 3: Costings 4 Worksheet
Q. 2 A damaged door is to be replaced including new hinges and lock. If the door costs € 35.80, the hinges and lock € 5.25 and the job takes a joiner 3 hours @ € 17.30 per hour, calculate the cost of the work allowing 25% for overheads and profit.
Answer:
Q. 2 Total Cost: Door € 35.80
Hinges € 5.25
Labour (3 x €17.30) = € 51.90
€ 92.95 + 25% = € 116.18

## Slide 4: Costings 4 Worksheet
Q. 3 The given drawing shows the plan and elevation of a simple roof. Using the rates below, which include the cost of materials and labour only, estimate the cost of felting, battening and tiling the roof. Add 25% for profit and a further 5% for overheads.
Roofing felt = € 7.10 per m²
Tiling Slopes = € 16.88 per m²
(including Battens)
Ridge tiling = € 4.16 per m run

## Slide 5: Costings 4 Worksheet
Q. 3 First get rafter length
a² + b² = c²
3² + 4² = x²
9 + 16 = x²
√25 = x = 5
  Area = 5 x 10 x 2 = 100m²
Cost: Roofing Felt 100 x € 7.10 = € 710.00
Tiling 100 x € 16.88 = € 1688.00
Ridge 10 x € 4.16 = € 41.60
€ 2439.60
€2439.60 +25%(profit) = 3049.5 x + 5%(overheads) = € 3,201.98
Answer: € 3,201.98
HYP is
the Rafter

## Slide 6: Costings 4 Worksheet
Q. 4 A room is 4.5m by 3.6m and 2.7m high. It has two doors (each 2200 x 1000mm including architrave) and one window (2400 x 1200mm). Estimate the cost of decoration as follows:
Ceiling to be painted with 2 coats emulsion @ € 5.40 per m²
Walls to be pre-paired and painted 2 coats @ € 6.00 per m²
Doors (room side only) painted 1 coat @ € 7.50 per m²
Allow 25% for overheads and profit.
(Prices shown are per m² per coat)

## Slide 7: Costings 4 Worksheet
Q. 4 A room is 4.5m by 3.6m and 2.7m high. It has two doors (each 2200 x 1000mm including architrave) and one window (2400 x 1200mm). Estimate the cost of decoration as follows:
Ceiling to be painted with 2 coats emulsion @ € 5.40 per m²
Walls to be pre-paired and painted 2 coats @ € 6.00 per m²
Doors (room side only) painted 1 coat @ € 7.50 per m²
Allow 25% for overheads and profit.
(Prices shown are per m² per coat)
I would sketch out a 3D model and put in the sizes
2.2 x 1m
2.2 x 1m
2.4 x 1.2m
4.5m
2.7m
3.6m

## Slide 8: Costings 4 Worksheet
Q. 4
Ceiling = 4.5 x 3.6 = 16.2m x 2(coats) x € 5.40 = €174.96
Walls (4) 2 x 4.5 x 2.7 = 24.3
2 x 3.6 x 2.7 = 19.44 = 43.74m²
Less Doors 2 x 2.2 x 1.0 = 4.4
Window 2.4 x 1.2 = 2.88 = 7.28m²
= 36.46m² x 2 x €6 = €437.52
Doors = 2.2 x 1.0 x 2 = 4.4 m² x €7.50= €33.00 = € 33.00
€ 645.48
€174.96 (ceiling) + €437 (walls) + €33 (doors) = €645.48
Total Cost € 645.48 + 25% (overheads) = €806.85
Answer: €806.85

## Slide 9: Costings 4 Worksheet
Q. 5 Calculate the cost of the timber at €187.10 per m³ for a job requiring the following:
Twenty four 3.6m lengths of 50mm x 180mm
14.4m run of 50mm x 75mm
3.6m run of 75mm x 200mm
Allow 23% for VAT on your answer.
Q. 5
24 of 3.6 x 0.05 x 0.18 = 0.7776 m³
14.4 x 0.05 x 0.075 = 0.0540 m³
3.6 x 0.075 x 0.2 = 0.0540 m³
0.8856 m³ x €187.10 = 165.70
(Plus VAT) 165.70 + 23% (VAT) = € 203.81
Answer: €203.81